## Slide 2: Agenda
Intro Raspberry Pi
Intro Arduino
Programming Arduino
Basic electronics
What to build ?

## Slide 3: Raspberry Pi
Low cost computer, ARM processor
OS
  Linux ports (Raspbian, PiDora, RaspBMC, …)
  Windows 10 coming soon (PI 2 only)
USB
Ethernet
GPIO
HDMI
Audio
Camera (CSI)
Display (DSI)

## Slide 4: Arduino
Microcontroller board (several types)
No OS, limited instruction set
Extensible hardware (ie. shields)
USB
Power
Digital Input /Output
Analog Input
I2C
Power

## Slide 5: Programming Arduino
Lots of examples available
in IDE (File – Examples)
Arduino IDE

## Slide 6: Programming Arduino
12
4
A2
Use case:
When pressing a button
a LED is switched on when an
object is within a certain range

## Slide 7: Programming Arduino
Called when a sketch starts.
Use it to initialize variables,
pin modes, start using libraries, etc.
Setup() will only run once.
setup()

## Slide 8: Programming Arduino
loop()

## Slide 9: Programming Arduino
http://arduino.cc/en/reference/homePage

## Slide 10: Programming Arduino
PWM
(Pulse Width Modulation)

## Slide 11: Basic electronics
Caution
Max 40 mA pin current
Recommended max. 20 mA pin current for continuous use

## Slide 12: Basic electronics
U = I x R

## Slide 13: Basic electronics
Resistor
Limit current

## Slide 14: Basic electronics
Resistor
Floating input
Arduino

## Slide 15: Basic electronics
Resistor
Pull-up
Arduino
5 V
10 KΩ

## Slide 16: Basic electronics
Resistor
Pull-up
Arduino
5 V

## Slide 17: Basic electronics
+ -
Diode

## Slide 18: Basic electronics
+
-
LED

## Slide 19: Basic electronics
I2C bus
Master - generates clock signal and initiates communication with slaves
Slave - receives clock and responds when addressed by the master

## Slide 20: Basic electronics
Breadboard

## Slide 21: What to build?